The scooter

Honda Dio

Manual device on operation preventive maintenance and repair

By Andrey Levkovich Aka Dusha

Mail To: dusha_.ko2@tut.by

INDEX

1. Reduction and arbitrary symbols

2. General instructions on repair

3. Identification

4. Description and the recommendation of

4.1 Recommendations regarding maintenance by

4.2 Recommendations regarding control of scooter

5. Maintenance and the general audit procedures and adjustment

5.1 Maintenance rate

5.2 Arrangement of the elements of the systems of control, nourishment, electrical equipment

5.3 Body elements (SK50M)

5.4 Adjustment of headlight

5.5 Adjustment of oil pump

5.6 Testing fuel pump

5.7 Cleaning air filter

5.8 Pressure testing of the end of the compression stroke

5.9 Checking brake linings

6. Power unit

6.1 Oil pump

6.2 Oil tank

6.3 Choke

6.4 Carburetor

6.5 Petalous valve

6.6 Fuel tank

6.7 Fuel pump

6.8 Air filter

6.9 Removal and installation of motor

6.10 Dismantling and assembling engine

6.11 Cylinder head, cylinder and piston

6.12 Jackets of power unit

6.13 Kick- starter

6.14 Variator

6.15 Main drive

6.16 Carter engine

7. Checking and the repair of power unit

8. Undercarriage

8.1 Front suspension and front brake (SK50M)

8.2 Checking of the knot of front brake

8.3 Torr system with disk front brake (SK50M)

8.4 Handle of gas

8.5 Rear suspension and rear brake

8.6 Shock absorber

9. Electrical equipment

9.1 Storage battery

9.2 Regulator of voltage (rectifier)

9.3 Generator

9.4 Interrupter (block CDI)

9.5 Ignition coil

9.6 Checking the lead angle of ignition

9.7 Starter

9.8 Sensor of fuel level

9.9 Sensor of oil level

9.10 Lock of ignition

9.11 Switch of the turn indicators of

9.12 Lamps

9.13 Steering switches of

9.14 Schematics of the electrical equipment

1. Reduction and arbitrary

symbols of reduction

OFF.................................... is switched off

ON.........................................vklyucheno

The arbitrary symbols

2. General instructions on repair

1. With the dismantling plot details in the appropriate order in order to facilitate the subsequent

assembling.

2. Before the fulfillment of works with the electrical equipment you will disconnect wire from

the negative terminal of storage battery.

3. Compulsorily substitute split cotter pins, sealing gaskets, ferrules, stuffing boxes and so forth

by the new.

4. If necessary it is necessary to bring the sealing composition for averting the leakages to the

sealing gaskets.

5. Thoroughly soblyudayte all technical specifications with respect to the values of the moment

of the delay of threaded connections. Compulsorily use a torque wrench.

6. Depending on the nature of the repair produced can be required the application of special

materials and special tool for the maintenance and the repair.

7. During the replacement of the burnt out safety devices it is necessary to trace so that the new

safety fuse would be calculated for the appropriate current strength.

3. Identification

Series numbers are substituted in the indicated in the figure places:

The scooters of firm Honda are differed from other stamps in terms of more durable (and heavier) construction and sufficiently long-lived motors, which are worse yielded to boosting. Are most common the scooters of family Dio (Dio, Dio SR, Dio City Movement and others). Are in series produced models Dio ZX and SuperDio ZX with the augmented engine, the disk brakes and the sport suspension, and also different poluseriynye Dio ZX - special modifications with the sport switchboards and the carburetors, even by the more forced motors with the disposed release, intensified by frame and suspensions. The weak place of the usual Dio are the anthers of front fork. Bursting, they pass mud inside the fork - as a result of bushing and feathers rapidly they are worn out and go out of order. Furthermore, usual Dio have a somewhat unsuccessful tuning of variator (with failure and pickup), which hampers calm ride. These deficiencies are corrected on the more expensive models Dio ZX. The scooters of family Tact are intended for the beginning drivers. The merits of scooters Honda include the vertical engine, which ensures larger than in analogs, road clearance, and, in combination with the more rugged construction, it makes it possible to use a machine not only around the city, but also under the poor road conditions. With 1996-97 the annual production of scooters Honda transferred into the Indian branches of firm, which was reflected in the quality of those completing and assembling of machines.

4. Description and recommendation.

4.1 Recommendations regarding the maintenance on the scooters should be used gasoline with the octane  number not lower than 92. In the system of separate lubricant is compulsory the use of special motor oil for the two-stroke engines. The tentative consumption of oil - about 1 l on 1000 km with a decrease in the oil level to the emergency reserve, lights up pilot lamp on the combination of instruments. Sparkplugs should be checked every 1-2 thousand. km of path. After path in 4-8 thousand km (depending on operating conditions) one should substitute sparkplug. The periodicity of servicing air filter is 500 km with the ride along the dusty roads. Transmission oil in the reducer of rear wheel should be substituted yearly.

4.2 some recommendations regarding control of scooter are examined below some distinctive special features of the scooters of foreign production.

1. with the zero-length launch and the acceleration from the low speed do not twist out to the refusal the knob of gas to avoid the lift of scooter to the rear wheel and the tilting. Especially this is dangerous during the contact into the hill or with the significant load on the baggage carrier.

2. because of the V-belt variator acceleration occurs with a constant frequency of the rotation of engine (close to the revolutions maximum power); therefore the speed of scooter compulsorily should be checked on the speedometer.

3. with the braking should be used a front, and rear brake. With the use only of rear brake is possible the heaping up of scooter sideways, only front - the unguided drift or revolution through the control.

4. small size of wheels and short base make scooter sensitive to the unevennesses of road and they require the specific strictness in control.

5. should be followed the height of the protector of tires and as needed substituted they. Ride on the scooter with the worn protector of wheels is extremely unsafe.

6. with the passage of turnings one ought not to discard gas in the turning in order to avoid of extension from the road. Turning should be passed "vnatyag", checking gas or to in advance discard it. Otherwise, with the sharp decrease of the frequency of rotation centrifugal cohesion does not manage to disconnect engine from the transmission and occurs intensive braking by engine.

7. always include lower beam with the ride on the scooter.

5. Maintenance and the general audit procedures and adjustment

Attention: in this management are used the following arbitrary symbols of the modifications of scooters Honda:

Honda Dio................SK50M

Honda Tact...................SZ50P

ST.............Standart (base model) As...... of..AutoStand (with the servodrive of support)

DB............... of..Disch Brake (with the disk brake) the attention: removal and dismantling it is main and aggregates it is achieved by way of the numbers, indicated in the figures. Assembling and installation are accomplished in the order, reverse to dismantling and to removal.

Servicing capacities:

Honda Dio The fuel tank........................... of.4,0 l

motor oil........................ of 0,8 l

the transmission oil......... of.0,09 l

Honda Tact The fuel tank... of 5,0 l (ST)/4,5 l (AS) motor oil........................ of 1,2 l

the transmission oil......... of.0,09 l

Fig. 3. recommended viscosity of motor oil

Carburetor

Carburetor............... PB80 (Dio) or PB80W (Tact): the diameter of the choke.................. of 14 mm

Frequency of the rotation of idling........................ by 1700-1900 r/min

Main jet......... of.№88 (Dio) or 78 (Tact)

Idle jet............ of.№35

Pressure in the tires: the front wheel............... of 1,25 kg/cm

the rear wheel.................. of.2,00 kg/cm.

Electrical equipment:

Storage battery. ............... 12V/ 3Ah

the lead angle of ignition............... 17 VMT of sparkplug:

Dio: NGK....................BPR5HS, BPR6HS, BPR7HS, BPR8HR

Denso.................. W16FPR, W20FPR, W22FPR, W24FPR

Tact: NGK....................BR4HSA, BR8HSA

Denso..................  W14FR-L, W24FR-L

Maintenance rate:

1000 km - checking and cleaning the air filter - checking and the adjustment of the rope of the gas - checking the brakes - pressure testing in the tires - checking the light instruments - checking sparkplugs through

3000 km - decarbonizing from the engine - checking the level of the transmission oil - checking the bearings of the steering column - checking and the adjustment of the ropes of the brakes - checking the brake linings - checking the storage battery - checking the wear of the tires - checking the fastening - the lubricant of ropes

6000 km - the replacement of sparkplugs - the replacement of the transmission oil - checking the front fork - checking the shock absorbers - cleaning the carburetor

Fig. 4. Arrangement Of the elements Of electrical equipment (SK50M).

1 - rectifier,

2 - the sensor of oil level,

3 - high-voltage wire,

4 - main plait of installation,

5 - ignition coil.

Fig. 5. arrangement of ropes and plaits of installation (SK50M)

. 1 - rope of front brake, 2 - rope of rear brake, 3 - resistor, 4 - installation of the lock of ignition, 5 - rope of gas, 6 - light switch, 7 - right plait of steering switches, 8 - left plait of steering switches, 9 - switch of the light of headlights, 10 - switch of turn indicators, 11 - switch of sound signal, 12 - wire of stop signal (from the lever of rear brake), 13 - wire of left turn indicator, 14 - wire of front headlight, 15 - wire of right turn indicator, 16 - wire of stop signal (from the lever of front brake).

Fig. 6. arrangement of ropes and plaits of installation (SK50M).

1 - the rope of speedometer, 2 - the basic plait of installation, 3 - rope of rear brake, 4 - rope of gas, 5 - hose of front brake.

Fig. 7. arrangement of the elements of the system of control (SK50M).

1 - the rope of gas, 2 - the rope of rear brake, 3 - rope of speedometer, 4 - rope of front brake, 5 - main plait of installation.

Fig. 9. arrangement of the elements of the system of control and nourishment (SK50M).

1 - plait of the installation of generator and starter,

2 - the rope of gas,

3 - the unit of safety devices,

4 - interrupter,

5 - relay of starter,

6 - wire of electric starter,

7 - left tube of the ventilation of crankcase,

8 - tube of the oil supply,

9 - rope of rear brake,

10 - control cable of oil pump,

11 - oil tube,

12 - wire of the sensor of fuel level.

Fig. 10. arrangement of ropes and plaits of installation (SK50M).

1 - the rope of speedometer, 2 - the installation of the lock of ignition, 3 - rope of gas, 4 - hose of front brake, 5 - rope of speedometer, 6 - rope of rear brake, 7 - yokes of wires, 8 - resistor, 9 - switch of starter, 10 - light switch, 11,12 - installation of steering switches, 13 - switch of the light of headlight, 14 - switch of turn indicators, 15 - wire of stop signal, 16 - wire of left turn indicator, 17 - wire of front headlight, 18 - wire of right turn indicator.

Fig. 15. lateral revetment.

1 - catch, 2 - lateral revetment, 3 - screws of the fastening

Fig. 16. front fairing.

1 - the screws of fastening, 2 - front fairing, 3 - front cover, 4 - screws of fastening, 5 - catch.

Fig. 17. lateral fairing.

1 - flanged nut, 2 - flanged bolt, 3 - rear baggage carrier, 4 - catch, 5 - lateral fairing, 6 - screws of fastening.

Fig. 18. outdoor revetment.

1 - catchs, 2 - the revetment of steps, 3 - clamp bolts.

Fig. 19. front cover.

1 - clamp bolt, 2 - front cover, 3 - catchs, 4 - screws of fastening.

Fig. 20. baggage hold.

1 - flanged bolts, 2 - padding, 3 - cover of oil tank, 4 - rear baggage carrier, 5 - flanged bolt, 6 - flanged nut, 7 - baggage hold.

Fig. 21. steering fairing.

1 - mirror of rear form, 2 - joints of the installation of front headlight and turn indicators, 3 - the screws of fastening, 4 - steering fairing, 5 - clamp bolt, 6 - catchs.

Fig. 22. rear wing.

1 - catch, 2 - the wire of rear turn indicator, 3 - rear wing, 4 - clamp bolts.

Fig. 23. LATERAL REVETMENT.

Fig. 24. steering fairing.

1 - the rope of speedometer, 2 - the tail end of the steering fairing, 3 - bolt, 4 - installation of steering switches, 5 - screws of fastening.

Fig. 25. Body Elements.

1 - lateral revetment, 2 - baggage hold, 3 - lateral fairing, 4 - outdoor revetment, 5 - rear wing, 6 - front fairing, 7 - front cover, 8 - steering fairing, 9 - the tail end of the steering fairing

Fig. 26. baggage hold.

1 - clamp bolt, 2 - the cover of tank, 3 - the packing washer, 4 - the baggage hold

Fig. 27. outdoor revetment.

1 - catch, 2 - clamp bolt, 3 - outdoor revetment, 4 - catch, wing, 3 - screws of fastening.

Fig. 28. front wing

1 - the screws of fastening, 2 - front

Fig. 29. front cover.

1 - the screws of fastening, 2 - clamp, 3 - clamp bolt, 4 - front cover, 5 - catch.

Fig. 30. lateral fairing.

1 - catch, 2 - fairing, 3 - rear baggage carrier, 4 - clamp bolt, 5 - rope, 6 - joints of wiring, 7 - screws of the fastening

Fig. 31. rear wing.

1 - clamp bolt of oil tank, 2 - relay, 3 - bracket, 4 - clamp bolt, 5 - interrupter (knot CDI), 6 - clamp, 7 - rear wing.

Fig. 32. adjustment of headlight Prover'te the direction of the light beam of front headlight and, if necessary, adjust it with the aid of the adjusting screw

Fig. 33. steering fairing.

1 - the screws of fastening, 2 - the screw of fastening, 3 - padding of master brake cylinder, 4 - steering fairing, 5 - mirror of rear form.

Fig. 34. the tail end of the steering fairing.

1 - joint of the switch of stop signal, 2 - joint of the switch of stop signal, 3 - joint of the installation of the combination of instruments, 4 - rope of speedometer, 5 - screws of fastening, 6 - joint of the switch of stop signal (ST, AS).

Fig. 35. adjustment of fuel pump.

1 - controlling lever, 2 - the housing of oil pump, 3 - marker, 4 - adjusting nut. You will completely unscrew the handle of gas (open the throttle) and prover'te, that the markers on the housing of oil pump and the controlling lever coincide. If necessary, adjust with the aid of the adjusting nut.

Fig. 36. testing fuel pump.

1 - carburetor, 2 - fuel tube, 3 - fastening. With the work of engine at the idling measure a quantity of fuel, supplied with pump for 10 s. Nominal volume.................. of 20 cc

5.7 cleaning of air filter

Wash the filtering element in washing oil, after which slightly finish harvesting and give completely to get dry. You will look around exterior view and state of porolon. If porolon has cracks and scalings, it should be replaced by the new filtering element. Wipe with the clean rags, moistened in the gasoline, the internal part of the cover of filter and the internal cavity of housing. You will look around the air duct of filter to the carburetor. The casing of filter and air duct must not have cracks. Impregnate the dry and clean filtering element before the installation in oil. For this use special oil for the impregnation, or another oil with a sufficient viscosity. You will distribute oil evenly along the filter, but do not twist out the filtering element. Filter is ready to installation if it abundantly it is impregnated with oil on the entire surface and the thickness.

5.8 pressure testing of the end of the compression stroke

1. Turn inside out sparkplug.

2. You will establish compressometer.

3. You will completely unscrew the handle of gas.

4. Measure the value of compression with cranking of crankshaft by the electric starter (frequency of rotation not less than 600 r/min), the nominal pressure......... of 10 kg/sq cm the reason for insufficient compression they can be:

a) The damage of the padding of the cylinder head,

b) The wear of piston rings, the damage of piston,

c) The wear of cylinder.

5.9 Checking of the brake linings

Prover'te the state of the brake linings.

a) press on the brake beams.

b) prover'te the position of indicator. If indicator exceeds the limits of the zone, shown in the form of marker, then should be replaced the brake linings.

6. Power unit

Attention: removal and dismantling it is main and aggregates it is achieved by way of the numbers, indicated in the figures. Assembling and installation are accomplished in the order, reverse to dismantling and to removal.

Fig. 37. oil pump. Removal and installation. 1 - oil tube, 2 - the tube of oil feed, 3 - clamp bolts of the bracket of control cable, 4 - control cable with the bracket, 5 - oil pump.

Fig. 38. oil tank. Removal and installation. (SK50M).

1 - oil tube, 2 - the joint of installation, 3 - nut of fastening, 4 - clamp bolt, 5 - rear wing, 6 - clamp bolt, 7 - oil tank.

Fig. 40. choke. Dismantling and assembling.

1 - choke, 2 - the rope of gas, 3 - spring of choke, 4 - padding, 5 - cover of carburetor, 6 - shielding cap, 7 - catch, 8 - locking needle, 9 - clamp.

Fig. 41. Carburetor. Removal and installation.

1 - choke, 2 - fuel tube, 3 - tube of oil feed, 4 - wire of starting enricher, 5 - clamp bolts of carburetor, 6 - O-ring seal, 7 - padding, 8 - O-ring seal, 9 - carburetor.

Fig. 42. Carburetor. Dismantling and assembling.

1 - cover of starting enricher, 2 - screws of fastening, 3 - about rate, 4 - starting enricher, 5 - O-ring seal, 6 - screws of fastening, 7 - float chamber, 8 - O-ring seal, 9 - axis of float, 10 - float, 11 - needle valve, 12 - screw of quality, 13 - idle jet, 14 - main jet, 15 - emulsion tube.

Fig. 43. petalous valve. Dismantling and assembling.

1 - clamp bolt, 2 - clamp bolt, 3 - protective housing, 4 - clamp bolts, 5 - inlet pipe, 6 - padding, 7 - petalous valve, 8 - padding.

Fig. 44. fuel tank. Removal and installation.

1 - the joint of installation, 2 - holder, 3 - sensor of fuel level, 4 - packing, 5 - fuel tube, 6 - clamp bolt, 7 - cover plate, 8 - fuel tank.

Fig. 45. fuel pump. Removal and installation (SK50M).

1 - fuel filter, 2 - fuel tube, 3 - fuel tube, 4 - vacuum hose, 5 - clamp bolt, 6 - fuel pump, 7 - nut of fastening, 8 - fuel pump bracket

Fig. 47. air filter. Removal and installation (SK50M).

1 - the screws of fastening, 2 - the cover of air filter, 3 - filtering element, 4 - screw of yoke, 5 - clamp bolts, 6 - casing of air of filter, 7 - vent pipe.

Fig. 49. removal and installation of motor (SK50M).

1 - installation of generator and electric starter, 2 - wire of starting enricher, 3 - oil tube, 4 - fuel tube, 5 - vacuum hose, 6 - cover of sparkplug, 7 - clamp bolt of rear shock absorber, 8 - control cable of oil pump, 9 - rope of rear brake, 10 - nut of fastening, 11 - clamp bolt, 12 - engine, 13 - bolt of the mounting bracket of engine, 14 - mounting bracket of the engine

Fig. 51. cylinder head, cylinder and piston. Removal and installation.

1 - clamp bolts of cylinder head, 2 - cylinder head, 3 - padding of cylinder head, 4 - cylinder, 5 - padding of cylinder, 6 - check rings, 7 - wrist pin, 8 - piston, 9 - piston rings, 10 - dilator of rings, 11 - needle bearing 12 - upper ring, 13 - lower ring.

Fig. 52. Jackets of power unit. Removal and installation.

- clamp bolts, rear jacket is 2nd, 3- padding, 4- clamp bolts, front jacket is 5th, 6- padding, 7- the dowel pin.

Fig. 53. Kick- starter. Removal and installation.

- drive gear, it is 2nd washer, 3- clamp bolt, 4- pedal of kick- starter, it is 5th check ring, 6- washer, 7- the gear quadrant of kick- starter, it is eighth return spring, 9 bushing.

6.13 checking is the kicks of starter

1. Verify kick- starter.

A) Verify splined bushing.

b) Verify the gear quadrant of kick- starter.

c) Verify   the gear   the drive of kick- starter.

Fig. 54. 1- drive gear, it is 2nd retaining spring, 3- the dowel pin.

Fig. 55

- Verify the beds of the axes of gear quadrant and drive gear.

Fig. 56.    1- splined bushing, it is 2- return spring, 3- bushing.

Fig. 58. Variator. Removal and installation.

- gear of electric starter, it is 2nd the nut of fastening, 3- bushing, 4- fixed cheek of guide pulley, V-belt is 5th, 6- nut of fastening the drum of cohesion, 7- drum of cohesion, the unit of cohesion and follower pulley is eighth, 9 muff of variator, 10 clutch of the variator

Fig. 59. Clutch of variator. Dismantling and assembling.

- clamp bolts, it is 2nd the cover of the clutch of variator, 3- the guiding plate, 4- guiding, it is 5th O-ring seal, 6- small weights, 7- mobile cheek.

Fig. 60. Unit of cohesion. Dismantling and assembling.

- nut of fastening, it is 2nd check ring, 3- washer, 4- boot-tree of cohesion, it is 5th the spring of the boot-trees of cohesion, 6- damper, 7- supporting disk, it is eighth the thrust bushing of spring, 9 spring of follower pulley, 10 bushing, 11- guide pin, 12- mobile cheek of follower pulley, 13- O-ring seal, 14- stuffing box, 15- bearing, 16- check ring, 17- bearing, 18- the fixed cheek

Fig. 61. Main drive. Dismantling and assembling.

- clamp bolt, it is 2nd the cover of reducer, 3- padding, 4- the dowel pin, it is 5th washer, 6- output shaft, 7- washer, it is eighth idlers, 9 washer, 10 input shaft.

Fig. 62. Removal of crankcase			Installation of crankcase

1. Turn away clamp bolts.				             1. You will install right bearing.

2. Remove the cover of crankcase.				2. You will install left bearing.

3. You will establish crankshaft.

4. You will establish the left stuffing

box

Fig. 64. Crankcase. Removal and installation.

- clamp bolts, it is 2nd the cover of crankcase 3- padding, 4- the dowel pin, crankshaft is 5th, 6- right stuffing box, 7- left stuffing box, right bearing is eighth, 9 left bearing.

7. Checking and the repair of power unit

1. You will clean cylinder head.

A) You will clean remainders of padding and carbon deposit from injector face. Note: you be careful, in order not to injure the injector face of cylinder, mated with the padding.

2. Verify cylinder head. By precision rule and by flat probe, as shown in figure, verify the nonplanarity of the working injector face of the cylinder

The maximum permissible non planarity of ..................... 0,02 mm

if the value of non planarity exceeds maximum permissible, you will replace cylinder head or grind it.

3.  You will clean carbon deposit from internal surface of exhaust of cylinder.

4. Verify cylinder.

A) By precision rule and by flat probe, as shown in figure, verify the non planarity of the surface of cylinder.

The maximum permissible non planarity of .................... 0,02 mm

if the value of non planarity exceeds maximum permissible, you will replace cylinder or grind it.

6) measure the diameter of cylinder.  Fig. 67

by Indicator- inside calipers measure the diameter of cylinder at three levels in transverse (a) and longitudinal (b) directions, as shown in figure. If the diameter more than maximum permissible, you will replace it.

Diameter of the cylinder:

SK50M

nominal .......... 39,000-39,020 mm

maximum .................... 39,050 mm

SZ50P

marker “A”

nominal .......... 39,000-39,005 mm

maximum of .................... 39,050 mi

without the marker

nominal .......... 39,005-39,010 mm

maximum .................... 39,050 mm

the maximum conicity of ...... 0,05 mm

5. You will clean piston.

A) By scraper remove carbon deposit

and others carbonic   the deposit   [s]   piston head.

b) You will clean deposits from grooves of piston with the piece of the broken ring.

c) By solvent and by soft hair brush you will finally clean piston.

Note: do not use wire brush.

6. Verify piston.

A) by micrometer measure the diameter of piston skirt of at a distance 4 mm rel.un. of edge, also, in the direction, perpendicular to the axis of wrist pin, as shown in Fig. 70.

Diameter of the piston:

SK50M

nominal ......... 38,955-38,970 mm

minimum ..................... 38,900 mm

SZ50P without the marker

nominal ......... 38,960-38,965 mm

minimum ..................... 38,900 mm

marker “A”

nominal ......... 38,955-38,960 mm

minimum ..................... 38,900 mm

marker “into”

nominal ......... 38,965-38,970 mm

minimum ..................... 38,900 mm

7.   You will determine clearance between the cylinder and the piston, after finding a difference in the results of the measurements of the diameter of piston and diameter of cylinder. The nominal clearance of ...... 0,035-0,050 mm

if clearance is more than nominal, you will replace piston and cylinder.

8.  Verify clearance in the piston-ring lock.

A) put piston ring into the cylinder up to the distance of 10 mm    from the parting plane.

b) by flat probe measure the clearance in the lock						Fig. 71

Nominal clearance of .......... 0,10-0,25 mm

The maximum clearance of ................ 0,40 mm

if clearance in the lock is more than maximum, you will replace piston ring. If clearance in the lock is more than maximum even with the new piston ring, you will replace cylinder and piston.

9. Verify end clearance “compression ring - piston groove”, after measuring by its flat probe, as shown in Fig. 73.

Nominal clearance of .......... 0,03-0,05 mm							Fig. 72

maximum clearance of ................ 0,10 mm

if   the clearance   it is more   permitted, you will replace piston.

10. Verify wrist pin. (Fig. 74)

a)    Put   piston   the finger   you will be convinced with the bearing into the connecting-rod end,    that    the finger    it pivots without the perceptible gap.

b)   By inside calipers,  measure the inside bore diameter under the finger in the piston.

Nominal										Fig. 73

diameter of .................... 12,002-12,008 mm

the maximum diameter of ...... 12,030 mm

c) using a micrometer, measure the diameter of wrist pin. Nominal diameter of .......... 11,994-12,000 mm

the minimum diameter of ....... 11,980 mm

if   it is necessary,   you will replace   piston and wrist pin in the collection.

11. Verify cohesion. 									Fig. 74

a)   Measure   internal   the diameter of the drum of cohesion.

The nominal diameter of ........................ 107,0-107,2 mm

the maximum diameter of ........ 107,5 mm

b) measure the thickness

of the friction lining.

Fig. 75								Fig. 76

Nominal thickness of ........ 4,0-4,1 mm

the minimum thickness of ............. 2,0 mm

12. Verify the clutch of variator.

a) Verify the surfaces of mobile and stationary cheeks.

b) Measure the diameter of bushing. The

nominal

thickness of .................. 20,035-20,085 mm

the minimum thickness of ....... 20,600 mm

c) Verify the diameter of roller.

Nominal diameter….15,92-16,08 mm

the minimum diameter of ......... 15,40 mm

13. Verify V-belt. (Fig. 77)

a) Verify the surface condition of belt (1).

b) Measure the width of belt (2).

Nominal width of ............... 15,5 mm					Fig. 77

Minimum width of ............... 14,5 mm

14. Verify follower pulley. (Fig. 78)

a) Verify surface condition    mobile    and    fixed of pulleys.

b) Verify and you will if necessary replace stuffing box.

c) Verify the smoothness of the rotation of pulley.

g) verify the length of unloaded spring.

Nominal length of .................. 98,1 mm

The minimum length of .................. 92,8 mm									Fig. 78

15. Verify electric starter.

a) Verify the state of flywheel and idlers.

16. Checking main drive.

a) Verify   the state   the driven gear of main drive shaft, idlers, slave gear.

b) Verify   the state   the radial bearings of driven gears.

17. Verify crankshaft.

a) Verify the bend of crankshaft. Maximum bend of .............. 0,04 mm

8. The undercarriage

Attention: removal and the dismantling of units and aggregates is achieved by way of numbers, indicated in the figure.

Assembling and installation is accomplished in the order, reverse to dismantling and to removal.

Fig. 79. Removal and the installation of front wheel (SK50M)

- Screw of fastening, the rope of speedometer is 2nd, 3- the  nut of front brake, 4- [vtupka] of brake beams, the rope of front brake is 5th, 6- nut of axis, 7- axle of front wheel, it is eighth bushing, 9 front wheel, 10 front wing, 11- unit of front brake, 12- anther, 13- left bearing, 14- the spacing collar, 15- right bearing.

8.2 checking of the unit of front brake

1.	Measure the free motion of brake beams and with

the need adjust it.

Nominal motion by .................... 10-20 mm

2. Measure the diameter of the internal surface

of brake drum.

Nominal diameter of ............ 95,0 mm

the maximum diameter of .......... 95,5 mm

3. Measure the thickness of the brake linings.

Nominal thickness of .............. 3,0 mm

the minimum thickness of .............. 2,0 mm

Fig. 80.

1- anther, left bearing is 2nd,

3- the spacing collar, 4- right bearing.

Fig. 81. Dismantling and the assembly of the unit of front brake (SK50M).

- brake shoes with the springs, clamp bolt is 2nd, 3- lever, 4- indicator of the wear of cover plates, it is 5th return spring, 6- unclasping fist, 7- stuffing box of unclasping fist, anther is eighth, 9 gear of speedometer, 10 housing of the unit of the front brake

Fig. 82. The steering column (SK50M).

Dismantling and assembling. 1- nut of fastening the steering column, it is 2nd upper lid, 3- the steering column, 4- lower cover, it is 5th bearings, 6- bearing cap, 7- clamp bolts, it is eighth fastening front wing, 9 clamp bolt, 10 front fork.

Fig. 83. Front fork (SK50M).

Dismantling and assembling. 1- cover of the feather of front fork, anther is 2nd, 3- check ring, 4- bushing, it is 5th the spring of the motion of return, 6- fixed pipe of the feather of front fork, 7- spring of the feather of front fork, rubber damper is eighth, 9 mobile tip.

8.3 Torr system with the disk front brake (SK50M)

Fig. 84. Front wheel. Removal and installation.

- screw of fastening the rope of speedometer, the rope of speedometer is 2nd, 3- the nut of axis, 4- wheel axle, it is 5th front wheel, 6- bushing, 7- drive of the speedometer

Handle of gas. Removal and installation.

- nut of fastening, the link bolt of the lever of front brake is 2nd, 3- the lever of front brake, 4- rope of front brake, clamp bolt is 5th, 6- the upper lid of the handle of gas, 7- bracket of the lever of front brake, the rope of gas is eighth, 9 handle of gas.

Fig. 85. Retarding disc. Removal and installation.

1- anther, right bearing is 2nd, 3- the spacing collar, 4- left bearing, it is 5th the clamp bolts of retarding disc, 6- retarding disc.

Fig. 86. Brake support. Removal and installation.

- clamp bolt, it is 2nd guide fingers, 3- the brake linings, 4- plate.

Fig. 87. Master brake cylinder (SK50M). Dismantling and assembling.

1- screws of fastening cylinder cover, it is 2nd cylinder cover, 3- the membrane, 4- bypass bolt and washer, brake hose is 5th, 6- the link bolt of brake beams, 7- brake beams, it is eighth the clamp bolts of holder, 9 holder of cylinder, 10 brake cylinder in the collection, 11- screws of fastening the switch of stop signal, 12- switch of stop signal, 13- bushing, 14- check ring, 15- valve, 16- spring.

Checking front disk brake

1. Measure the free motion of brake beams and if necessary adjust it.

Nominal motion by ................... 10-20 mm

2. Measure the diameter of the piston of master brake cylinder.

Nominal diameter of ............ 10,957-10,984 mm

the minimum diameter of ....... 10,910 mm

3. Measure the diameter of master brake cylinder.

Nominal diameter of .................... 11,000-11,043 mm

the maximum diameter of ........ 11,05 mm

4.  Measure the diameter of the piston of front, brake.

Nominal diameter of .................... 30,148-30,198 mm

the minimum diameter of ........ 30,290 mm

5.   Measure the diameter of the cylinder of front brake.

Nominal diameter of .................... 30,230-30,280 mm

the maximum diameter of ........ 11,05 mm

6. Measure the thickness of retarding disc.

Nominal thickness of .............. 3,0 mm

the minimum thickness of .............. 2,5 mm

Fig. 88. Support of front brake (SK50M). Dismantling and assembling.

- bypass bolt and washer, it is 2nd the cover of guide of finger, 3- the clamp bolts of support, 4- Torr support, it is 5th the guide fingers of boot-trees, 6- brake shoes, 7- adjusting plate, it is eighth unclasping spring, 9 guide finger, 10 bracket of support, 11- cover of guide of finger, 12- bushing, 13- piston, 14- case, 15- collar.

8.4 Rear suspension and the rear brake

Fig. 89. Dismantling and assembling rear brake.

1-adjusting nut, it is 2nd the bushing of lever, 3- the rope of rear brake, 4- brake shoes with the springs, the clamp bolt of lever is 5th, 6- lever of rear brake, 7- return spring, the indicator of the wear of the brake linings is eighth, 9 stuffing box, 10 unclasping fist, 11- travel limiter of boot-tree.

Fig. 90. Removal and the installation of shock absorber.

- lower clamp bolt, upper clamp bolt is 2nd, 3- rear shock absorber.

Fig. 91. Dismantling and assembling shock absorber.

- bushing, it is 2nd the grommet, 3- the lower opening of fastening, 4- spring, it is 5th the lock nut, 6- rubber damper, 7 - седло пружины, shock absorber is eighth.

1. Remove bushing.

2. Remove the grommet.

3.  Remove the lower opening of fastening.

4. Remove spring.

5. Turn away the lock nut.

6. Remove rubber damper.

7. Remove the saddle of spring.

8. Remove shock absorber.

Assembling shock absorber is produced in the order, reverse to its dismantling.

FIG. 93

9. Electrical equipment is

Note. For the designation of the colors of wires the following reductions are used: B is white, Ch is black, Kr - red, [Kch] - brown, Zh is yellow, With dark-blue, 3- green, [Rz] - pink, Sr - gray, About the orange, TZ - dark green, [TKch] - dark brown.

In this case the first part of the designation indicates the primary color of wire, the second (if there is) - the color of strips.

Fig. 94. Arrangement of the elements of electrical equipment.

- interrupter, rectifier is 2nd, 3- of the relay of starter, 4- storage battery, electric starter is 5th, 6- it soaked ignitions, 7- switch of sound signal, the switch of turn indicators is eighth, 9 switch of the light of headlight, 10 light switch, 11- switch of starter, 12- resistor, 13- winding of ignition, 14- alternator, 15- ignition coil, 16- ignition coil.

9.1 The storage Battery

Fig. 95.

- screws of fastening the cover of storage battery, it is 2nd cover, 3- negative terminal, 4- positive terminal, it is 5th storage battery.

FIG. 97                                                               FIG. 96

Checking storage battery

1.	Verify stress on the outputs of storage battery,   if   it lower than nominal, you will load storage battery. (Fig. 96)

nominal stress. 13,0-13,2 [v]

minimum stress ......... 12,3 [v]

2.	Verify with the aid of the ammeter the absence of closing to the mass of electrical equipment.

Maximum current of ........................ 1 mA (Fig. 97)

9.2 Regulator of voltage (rectifier)

verify resistance between the outputs of the rectifier

FIG. 98

9.3 Generator

Checking on the engine

Verify stress,   issued by generator.

a) You will neglect engine.

b) You will include illumination, the switch of the light of headlights - to the position “HI”.

c) Measure the stress.

Nominal stress

(with 5000 aboutmin) ................ 12,6-13,6 [v]

FIG. 99

Fig. 100. Dismantling and assembling generator.

- clamp bolt, fan housing is 2nd, 3- clamp bolt, 4- cooling-system fan, it is 5th flanged nut, 6- rotor (flywheel), 7- key, the wire of generator is eighth, 9 joint of starter, 10 clamp bolt, 11- clamp bolt of pulse generator, 12- pulse generator, 13- clamp bolt of stator, 14- stator, 15- the protective bushing

Checking Generator

1.  Verify winding impedance of generator.

Nominal resistance:

The winding of charging .............. 0,2-1,0 Ohm is

the windings of illumination ......... 0,1-0,8 Ohm

2.  Measure the resistance of resistor.

Nominal resistance:

6,7 0[m], 5[Vt] of ...................... 4,7-5,3[Om]

5,9 Ohm, 30 W .................... 5,6-6,2 Ohm

Fig. 101

9.4 interrupter (block CDI)

Measure the resistance between the conclusions of the joint of the interrupter:

Wire 	                        Resistance, Ohm are

Excitation winding	     black- redgreen	                  500-900

Pulse generator	     dark-blue- yellowgreen	       50-200

Ignition coils	     black- yellowgreen	                    0,2-0,3

9.5 Ignition coil

Measure the resistance

of the primary winding of ignition coil.

Nominal resistance:

Dio ...................................... 0,2-0,3 Ohm

Tact .................................... 0,1-0,4 Ohm

Measure   the resistance

the secondary winding of ignition coil.

Nominal resistance:

with the tip of the spark plug:

Dio .................................... 8,2-9,3 kilohms

Of tact of ................................. 6,35-9,7 kilohms

without the tip of spark plug… 2,7-3,4 kilohms				Fig. 102

Fig. 103							Fig. 104

9.6 Checking   the angle   ignition advance

Verify the lead angle of ignition

with the frequency of rotation 1800 aboutmin.

Nominal lead angle

of the ignition of ........ 17±3°[doVMT]

Fig. 105

9.7 The Starter

Fig. 106. Removal and the installation of starter.

- clamp bolt, the bracket of control cable of oil pump is 2nd, 3- the clamp bolt of starter, 4- starter, it is 5th O-ring seal, 6- joint of starter.

Fig. 107. Dismantling and assembling starter.

- clamp bolt, stator is 2nd, 3- anchor, 4- brush holder, it is 5th spring, 6- O-ring seal, 7- front cover of starter.

9.8 Sensor of Fuel Level

Measure the resistance between the outputs

of the sensor of fuel level with different

position of float.

FIG. 108

Conclusions	                               Position of the float

upper	                    lower

green- yellowwhite	                    	25-41 Ohm		450-750 Ohm

green- are dark-bluewhite	       	430-700 Ohm		25-41 Ohm

are yellowwhite- dark-bluewhite	450-750 Ohm		450-750 Ohm

9.9 sensor of oil level

You will connect ohmmeter and will ascertain that with the upper position of float there is no conductivity, and with the lower position - there is conductivity between the outputs of sensor.

Fig. 109

9.10 lock of ignition

Prover'te conductivity between the outputs of the lock of ignition with its different positions, as shown in diagram

FIG. 110

9.11 Switch of turn indicators

Prover'te conductivity between the outputs of the switch of turn indicators with its different positions, as shown in diagram.

FIG. 111

9.12 lamps

Fig. 112. front headlight			 Fig. 113. Illumination of the combination of the

instruments

FIG 114    1 - bolt, 2 - the lock of ignition, 3 - joint of the lock of ignition.

9.13 The steering switches

Prover'te conductivity between the outputs of light switch with its different positions, as shown in diagram.

FIG 115

Top of Form Prover'te conductivity between the outputs (zheltyy/krasnyy and green) of the switch of starter with its switch oned position.

Bottom of Form

FIG. 116 Prover'te conductivity between the outputs of the switch of sound signal with its switch oned position. Prover'te conductivity between the outputs of the switch of the light of headlights with its different positions, as shown in diagram.

FIG. 117

Fig. 118. backing lamp.

1 - lamp of rear turn indicators, 2 - lamp of stop signal, 3 - glass- stop signal, 4 - screws of fastening, 5 - glass- turn indicator.

Fig. 119. arrangement of the elements of the system of the drive of support.

1 - the relay of generator, 2 - the relay of the system of drive, 3 - joint of magnetic valve, 4 - magnetic valve, 5 - lock of ignition, b - buzzer, 7 – servo drive, 8 - knot of the support

Fig. 120. schematic of the system of drive.

1 - storage battery, 2 - the safety device of yShcha, 3 - lock of ignition, 4 - relay of generator, 5 - generator, 6 - magnetic valve, 7 - buzzer, 8 - switch of drive, 9 - servodrive, 10 - relay of the system of drive.

Ris.121. Schematic of electrical equipment (Dio SK50M).

1 - the switch of stop signals, 2 - the switch of starter, 3 - light switch, 4 - lock of ignition, 5 - relay of starter, 6 - storage battery, 7 - regulator of voltage (rectifier), 8 - sensor of fuel level, 9 - sensor of oil level, 10 - right rear turn indicator, 11 - stop signal and rear dimensional fire, 12 - left rear turn indicator, 13 - sparkplug, 14 - interrupter (knot CDI), 15 - starting enricher, 16 - generator, 17 - electric starter, 18 - resistor, 19 - sound signal, 20 - switch of the light of headlight, 21 - switch of turn indicators, 22 - sound signal, 23 - relay of turn indicators, 24 - left front turn indicator, 25 - front headlight, 26 - right front turn indicator, 27 - combination of instruments, 28 - lamp of illumination, 29 - level indicator of fuel, 30 - the pilot lamp of the oil level, 31 - the pilot lamp of exceeding allowable speed, 32 - the safety device of "A, 33 - ignition coil